## Slide 1: Variable Length RRT (VLRRT)
Allows for extensions of varying lengths
Collects on the fly information about the world to vary the extension length:
  Each node has a weight ε that multiplies by the base ext. length
  Nodes in potentially less cluttered regions will have a higher ε value
  Intuition: Larger steps in uncluttered regions, smaller steps in cluttered ones.
How can we learn the values for ε at each node?
E
Random point
Node
d * ε
E
Node
d * ε
E
ε
ε'
ε'
On success
Increase ε
and continue

## Slide 2: Variable Length RRT (VLRRT)
How can we learn the values for ε at each node?
E
Random point
Node
d * ε
ε
On failure
Decrease ε
and continue
E
Node
d * ε’
ε'
If extensions succeed, its more likely that the region is uncluttered and so we scale up ε accordingly (and propagate to the new node).
If extensions fail, its less likely that the region is uncluttered and we scale back ε.
Abstracts away much of the topology of the world (can over- and under-estimate!)

## Slide 3: Directional VLRRT (DVLRRT)
Builds on the idea of VLRRT by taking into account direction of extensions.
Nodes no longer have a single ε value, but a directional map m(Θ) of values .
Abstracts away less of the topology to (hopefully) increase accuracy.
How do we use and populate the directional map?
E
Random point
Node
m
Θ
If m(Θ) is
defined
E
Random point
Node
m
Θ
E
d * m(Θ)
Increase m(Θ) on success
If m(Θ) is defined, try to extend by the corresponding value
Increase m(Θ) on success and decrease on failure.

## Slide 4: Directional VLRRT (DVLRRT)
How do we use and populate the directional map?
If m(Θ) is not defined, we compute it using the closest values in the map within the [Θ-π/2 , Θ+π/2] range.
Assign more weight to closer directions (more reliable estimate):
E
Random point
Node
m
Θ
If m(Θ) is
not defined
E
Node
m
Θ1
Θ2
E
Random point
Node
m
E
D*ε
If the extension succeeds, scale up m(Θ). Else scale it down.
New nodes inherit m(Θ) = ε and m(Θ+π) = ε into their directional maps.

## Slide 5: Evaluating VL and DVLRRT
We have yet to specify how to increase and decrease ε values:
  Empirical results show best performance with a high increase rate and a higher decrease rate.
We compared the performance of our algorithms with RRT in terms of running time and success in reaching the goal in several worlds:
Algorithm | World | Avg. Success | Avg Time (ms)
RRT | obstructed | 95% | 12.0
VLRRT | obstructed | 96% | 13.3
DVLRRT | obstructed | 96% | 13.4
RRT | maze | 91% | 17.2
VLRRT | maze | 99% | 10.6
DVLRRT | maze | 99% | 10.6
RRT | cluttered | 33% | 39.2
VLRRT | cluttered | 60% | 33.6
DVLRRT | cluttered | 60% | 33.7

## Slide 6: Evaluating VL and DVLRRT
The data shows that our algorithms perform similarly in worlds where RRT performs well
Our algorithms outperform RRT in situations where it does not fare well!
Adapting by using the information collected over time is better for planning.
Can we obtain similar gains in replanning? How can we use the gathered data to inform replanning?